## Slide 1: Multi-band photometric stereo using random sampling of channels and pixels
Daisuke Miyazaki
Koumei Hamaen
Hiroshima City University

## Slide 2: Photometric stereo
3 grayscale images
Surface normal estimation
3 unknowns

## Slide 3: Color photometric stereo
1 color image
RGB lights
One shot
Measurable: Dynamically deforming object

## Slide 4: Multispectral photometric stereo
1 multispectral image
Our approach
Robust to shadow

## Slide 5: Ambiguity of multispectral PS
Albedo
Intensity
Light
Normal
1
2
1
2
60°
cos60°
1
1
1
0°
cos0°
Solvable if the object is white (uniform albedo)

## Slide 6: 7 equations, 9 unknowns
Albedo
Intensity
Light
Normal
:Pixel brightness
:Diffuse albedo
:Surface normal vector
:Light direction vector
Equations 7
Unknowns 9: A0,A1,...,A6,nx,ny
Unsolvable

## Slide 7: Our approach
Proposed method
Random sampling
Fyffe et al. [8]
Region segmentation
Miyazaki et al. [17]
Median filter
Guo et al. [10]
Achromatic objects
Anderson et al. [1]
Shape from other sensors
Kim et al. [14]
Optical flow

## Slide 8: 1 channel, 1 pixel
Albedo
Intensity
Light
Normal
Input
Known
1 unknown
2 unknown
1 equation, 3 unknowns -> Unsolvable
If 1 channel and 1 pixel is chosen
Notes: これが画像の輝度の話です。
1チャンネル1画素選択した場合です。
式は、画素の輝度はアルベド×法線×光源であらわされます
ここで、入力は画素の輝度、光源は既知、未知数はアルベド1個、法線の未知数2個に対して
式が１つなので解くことができません

## Slide 9: 4 channels, 8 pixels
Surface normal is determined
Assuming same albedo among 8 pixels
32 equations, 20 unknowns
Equations: 4 x 8 = 32
Albedo: 4
Normal: 2 x 8 = 16
Solvable
Notes: 選んだ4チャンネルと8画素選択から法線推定をしました
そこから、

## Slide 10: Choose 8 pixels randomly
Interest pixel
3×3
7×7
13×13
21×21
29×29
41×41
55×55
We have to choose same albedo pixels
Near pixels have high possibility: Same albedo
Not always true
Randomly choose

## Slide 11: Choose 4 channels randomly
Diffuse reflection
Specular reflection
Shadow
Some channel includes shadows and speculars
Brighter channels have high possibility: Non shadow
Not always true
Randomly choose
Notes: チャンネルによるノイズを回避するために
輝度を用いてランダムにチャンネルを選択するようにした
輝度が高いほど選ばれやすくした

## Slide 12: Calculated surface normal
True normal
Calculated normal
(constant albedo)
Calculated normal
(variable albedo)
Same albedo
Different albedo
Interest pixel
Chosen pixel
Notes: これが推定される法線の一例です
しんのほうせん
チャンネル内のアルベドが一定であれば正しく推定できる
しかし、チャンネル内のアルベドが一定では無ければ正しく推定できない

## Slide 13: Surface normal candidate
Choose another set of 4 channels, 8 pixels
Correct
Outlier
64 candidates of surface normal
Outlier removal of candidate
Candidates of surface normal
Final surface normal
Notes: 選択した画素がアルベドが同一であれば解くことができます
ランダムに選択して条件がよければ解ける
ここでは、注目画素１つに対して2画素選択して3チャンネル選択した例です。

## Slide 14: 1 multispectral camera 7 multispectral light
Multiband camera
Light 0: 750 nm
Light 1: 632 nm
Light 2: 610 nm
Light 3: 550 nm
Light 4: 520 nm
Light 5: 470 nm
Light 6: 430 nm

## Slide 15: Simulation result
Albedo
Input
Ch. 0
Ch. 1
Ch. 2
Ch. 3
Ch. 4
Ch. 5
Ch. 6
3 channel, 4 pixels
4 channel, 8 pixels
4 channel, 16 pixels
7 channel, 16 pixels
Ground truth

## Slide 16: Evaluation
Photometric stereo
Proposed method
0
1.57
Error
[rad]
(Color photometric stereo
with white object)
(4 channels, 8 pixels)

## Slide 17: Glove result
Ch. 0
Ch. 1
Ch. 2
Ch. 3
Ch. 4
Ch. 5
Ch. 6
3 channel, 4 pixels
4 channel, 8 pixels
4 channel, 16 pixels
7 channel, 16 pixels

## Slide 18: Doll result

## Slide 19: Conclusion
Multispectral photometric stereo
Non-white object
Random sampling approach
More elegant sampling than random sampling
Conclusion
Future work

## Slide 20: Daisuke Miyazaki 2022 Creative Commons Attribution 4.0 International License.
http://www.info.hiroshima-cu.ac.jp/~miyazaki/
Daisuke Miyazaki, Koumei Hamaen, "Multi-band photometric stereo using random sampling of channels and pixels," IW-FCV2022, 2022.02